MATERIAL SAFETY DATA SHEET

SECTION l PRODUCT IDENTIFICATION

MANUFACTURER:.         SUPPLIER:

Multi-Blend Ltd

2720 Slough Street

Mississauga

Ontario L4T 1G3

EMERGENCY TEL: 613-996-6666

PRODUCT NAME: DELIMING SOLUTION

CHEMICAL NAME: NA

CHEMICAL FAMILY: HYDROCHLORIC ACID

PRODUCT USE: DELIMING,

SECTION ll HAZARDOUS INGREDIENTS

==================================================

HAZARDOUS-   APPROX-  CAS NO.      LD(50)                 LC 50

INGREDIENTS    CONC.                    (RAT ORAL)      Inhalation rat

==================================================

HYDROCHLORIC

ACID                      10-30         7647-01-0     900 mg/Kg     3124 ppm/1 Hr

SECTION lll PHYSICAL DATA

PHYSICAL STATE............LIQUID

ODOUR AND APPEARANCE.... PUNGENT ODOUR, CLEAR LIQUID

ODOUR THRESHOLD...........ND

SPECIFIC GRAVITY..........1.01

VAPOUR PRESSURE...........NE

VAPOUR DENSITY(air=1).....NE

EVAPORATION RATE..........>1

SOLUBILITY IN WATER.......COMPLETE

BOILING POINT.............92 DEG.. C

pH........................1.5

COEFF. WATER/OIL DISTR....NA

SECTION lV FIRE AND EXPLOSION DATA

CONDITIONS OF FLAMMABILITY.....NOT FLAMMABLE

EXTINGUISHING MEDIA............CARBON DIOXIDE, DRY CHEMICAL, FOAM, WATER

SPECIAL PROCEDURES.............FIREFIGHTERS SHOULD WEAR SELF CONTAINED BREATHING APPARATUS

FLASH POINT (DEG.)C.............NONE

HAZARDOUS COMBUSTION PRODUCTS..NA

UPPER FLAMMABLE LIMIT..........NA

LOWER FLAMMABLE LIMIT..........NA

AUTO IGNITION TEMP.............NA

EXPLOSION DATA.................NA

SENSITIVITY TO STATIC CHARGE...NA

SECTION V REACTIVITY DATA

CHEMICAL STABILITY.............STABLE

CONDITIONS TO AVOID............EXCESSIVE HEAT, SPARKS AND OPEN FLAME

INCOMPATIBLE SUBSTANCES........ALKALIES, COMBUSTIBLE MATERIALS, OXIDIZING AGENTS, REDUCING MATERIALS, CYANIDES, SULFIDES, FORMALDEHYDE.

HAZARDOUS DECOMPOSITION........HYDROGEN GAS

HAZARDOUS POLYMERIZATION.......WILL NOT OCCUR

SECTION Vl TOXICOLOGICAL PROPERTIES

ROUTE OF ENTRY

SKIN CONTACT.....YES  SKIN ABSORPTION..YES

EYE CONTACT......YES  INHALATION.......YES

INGESTION........YES

EFFECTS OF ACUTE EXPOSURE TO MATERIAL: SKIN: MAY CAUSE SEVERE CHEMICAL BURN AND OR DERMATITIS. EYE CONTACT: CONTACT WILL CAUSE SEVERE IRRITATION, PAIN, WITH CORNEAL INJURY, WHICH MAY RESULT IN PERMANENT EYE DAMAGE, BLINDNESS AND IMPAIRMENT OF VISION. INHALATION: DIRECT AND REPEATED BREATHING OF VAPOURS MAY CAUSE SEVERE IRRITATION AND INJURY TO THE UPPER RESPIRATORY TRACT AND LUNGS, EVEN DEATH.  INGESTION: WILL CAUSE BURNS OF MOUTH AND OESOPHAGUS AND GASTROINTESTINAL IRRITATION.

EFFECTS OF CHRONIC EXPOSURE: SEE ABOVE. MAY ALSO CAUSE EROSION OF TEETH, BLEEDING AND ULCERATION OF NOSE,  MOUTH AND GUMS.

EXPOSURE LIMITS................SEE SECTION ll. ACGIH TLV AND OSHA PEL ARE 5 ppm CEILING.

IRRITANCY OF MATERIAL..........CORROSIVE TO EYES AND SKIN

SENSITIZATION TO MATERIAL......SKIN & MUCOUS MEMBRANES

CARCINOGENICITY..........ND REPRODUCTIVE TOXICITY..........ND

TERATOGENICITY.................ND  MUTAGENICITY...................ND

SYNERGISTIC PRODUCTS...........ND

SECTION Vll PREVENTIVE MEASURES

HAND PROTECTION................PVC OR RUBBER

EYE PROTECTION.................FACE SHIELD IF CONTACT POSSIBLE

RESPIRATORY PROTECTION.........NORMAL VENTILATION ADEQUATE OTHERWISE NIOSH APPROVED RESPIRATOR FOR ORGANIC ACIDS.

FOOT WEAR......................RUBBER OR SIMILAR

CLOTHING.......................RUBBER OR NEOPRENE TO PROTECT REGULAR CLOTHING

ENGINEERING CONTROLS...........LOCAL EXHAUST ADEQUATE, MECHANICAL VENTILATION REQUIRED  IF WORKING WITH LARGE QUANTITIES IN A CONFINED SPACE.

LEAK AND SPILL PROCEDURE.......WEAR APPROPRIATE CLOTHING, VENTILATE AREA. SMALL SPILLS CAN BE NEUTRALIZED WITH LARGE AMOUNTS OF WATER AND FLUSHED. LARGER SPILLS SHOULD BE CONTAINED AND PICKED UP WITH INERT ABSORBENT MATERIAL AND TRANSFERRED TO RECOVERY CONTAINER. NEUTRALIZE REMAINDER WITH SODA ASH.

WASTE DISPOSAL.................IN ACCORDANCE WITH MUNICIPAL AND PROVINCIAL REGULATIONS

HANDLING PROCEDURES AND EQUIPMENT..AVOID SKIN AND EYE CONTACT

STORAGE REQUIREMENTS...........0-40 deg.. C KEEP FROM FREEZING, KEEP CONTAINER SEALED AND AWAY FROM HEAT, OPEN FLAMES AND INCOMPATIBLE MATERIALS.

SECTION Vlll FIRST AID MEASURES

PROCEDURES: EYES: IMMEDIATELY WASH WITH WATER FOR 15 MINUTES. SEEK MEDICAL ATTENTION IF IRRITATION PERSISTS. SKIN: IMMEDIATELY FLUSH AREA WITH COPIOUS AMOUNTS OF WATER THEN WASH WITH SOAP OR MILDLY ALKALINE SOLUTION SUCH AS 2.5% SODIUM BICARBONATE SOLUTION. IF REDDENING OR IRRITATION PERSISTS SEEK MEDICAL ATTENTION. INGESTION: DO NOT INDUCE VOMITING. DRINK LARGE AMOUNTS OF MILK IF AVAILABLE OR WATER. ANY KIND OF ANT-ACID TABLETS OR POWDER SHOULD BE TAKEN. SEEK MEDICAL ATTENTION IMMEDIATELY.

ADDITIONAL INFORMATION

WHMIS CLASSIFICATION...CLASS E, CLASS D DIV 2B

TDG CLASSIFICATION.....CLASS 8

SHIPPING NAME CORROSIVE LIQUID N.O.S. (HYDROCHLORIC ACID)

PIN....................UN 1760   PACKING GROUP..........ll

HAZARD RATING: HEALTH: 2   FIRE: 0   REACTIVITY :2   SPECIAL:

HAZARD RATING SCALE: 0=MINIMAL, 1=SLIGHT, 2=MODERATE, 3=SERIOUS, 4=SEVERE.

NA=NOT APPLICABLE, ND=NO DATA AVAILABLE, NE=NOT ESTABLISHED, NR NOT REGULATED.

PREPARED BY: LAB GROUP   DATE: 20 September 2005

TEL: 905-678-9559

DISCLAIMER: THE INFORMATION CONTAINED HEREIN IS COMPILED FROM SOURCES BELIEVED TO BE RELIABLE. THE MANNER AND CONDITIONS OF USE AND HANDLING MAY INVOLVE OTHER AND ADDITIONAL CONSIDERATIONS. WE ACCEPT NO RESPONSIBILITY FOR THE ACCURACY, SUFFICIENCY, RELIABILITY OF THIS INFORMATION AND DISCLAIMS ANY LIABILITY INCURRED IN CONNECTION WITH THE USE OF THIS PRODUCT OR THE DATA GIVEN ABOVE.