MATERIAL SAFETY DATA SHEET

SECTION l PRODUCT IDENTIFICATION

MANUFACTURER:         SUPPLIER:

Multi-Blend Ltd.

2720 Slough Street

Mississauga

Ontario L4T 1G3

EMERGENCY TEL: CANUTEC 613-996-6666

PRODUCT NAME: Bleach 5

CHEMICAL NAME: SODIUM HYPOCHLORITE

CHEMICAL FAMILY:CHLORINE

PRODUCT USE:Industrial cleaner

SECTION ll HAZARDOUS INGREDIENTS

HAZARDOUS-               APPROX-         CAS NO.          LD(50)                LC(50)

INGREDIENTS              CONC.%                                    (Mouse)             Inhalation rat

Sodium Hypochlorite    5-7                  7681-52-9      5800 mg / Kg    293 PPM / 1 Hour

SECTION lll PHYSICAL DATA

PHYSICAL STATE.............Liquid

ODOUR AND APPEARANCE....chlorine odour, green -yellow liquid

ODOUR THRESHOLD............ND

SPECIFIC GRAVITY...........1.165

VAPOUR PRESSURE............17.5 MmhG AT 20 deg C

VAPOUR DENSITY(air=1)......ND

EVAPORATION RATE...........ND

SOLUBILITY IN WATER........(20 deg C) Complete

BOILING POINT...Slowly decomposes at 40 C to NaCl and NaClO3

pH.........................12.5 - 13.5

COEFF. WATER/OIL DISTR.....ND

SECTION lV FIRE AND EXPLOSION DATA

CONDITIONS OF FLAMMABILITY.....Non-Flammable

EXTINGUISHING MEDIA............As for surrounding materials

HAZARDOUS COMBUSTION PRODUCTS..traces of chlorine

SPECIAL PROCEDURES......Full protection equipment, including a self contained breathing apparatus should be worn. Remove storage vessels from fire zone if possible. Use water spray to cool containers.

FLASH POINT (DEG)C.............NA

UPPER FLAMMABLE LIMIT....NA  LOWER FLAMMABLE LIMIT...NA

AUTO IGNITION TEMP.............NA

EXPLOSION DATA.................NA

SENSITIVITY TO STATIC CHARGE...ND

SECTION V REACTIVITY DATA

CHEMICAL STABILITY..........Unstable above 40 C, sunlight and contact with metals.

CONDITIONS TO AVOID............Temperatures above 40 C

INCOMPATIBLE SUBSTANCES........Strong acids,ammonia, strong oxidizing agents, may react with aluminium to form hydrogen.

HAZARDOUS DECOMPOSITION........ Hypochlorites may react with primary amines to form nitrogen trichloride which explodes spontaneously in air. Hypochlorite bleach reacts with urea to form nitrogen trichloride which explodes spontaneously in air. Some metals accelarate the decomposition of Sodium Hypochlorite. Nickel. Copper. Tin. Iron and its alloys. Manganese.

HAZARDOUS POLYMERIZATION.......Will not occur.

SECTION Vl TOXICOLOGICAL PROPERTIES

ROUTE OF ENTRY

SKIN CONTACT.....Yes  SKIN ABSORPTION..Yes

EYE CONTACT......Yes  INHALATION.......Yes

INGESTION........Yes

EFFECTS OF ACUTE EXPOSURE TO MATERIAL:

Eyes: Contact may cause severe irritation, ulceration of eyes, permanent visual damage may occur.

Skin: Contact may cause irritation, burns and blisters. Prolonged contact may bleach skin or cause dermatitis.

Inhalation: Corrosive to respiratory passages. Causes irritation of the mouth, nose and throat. Repeated and/or prolonged exposures may cause productive cough, running nose, bronchopneumonia, pulmonary edema (fluid buildup in lungs) and reduction of pulmonary function. If mixed with acids or warmed to temperatures greater than 40 degrees Celsius, Sodium hypochlorite solutions release chlorine gas. This gas can cause severe irritation of the nose and throat. Exposures to high levels of chlorine gas may result in severe lung damage.

Ingestion: Corrosive. Causes burns to the mouth, throat and stomach. Causes vomiting, nausea, and diarrhea.

Coma, shock and death may occur.

EFFECTS OF CHRONIC EXPOSURE: ND

EXPOSURE LIMITS................See Section II

ACGIH  0.5 ppm as for chlorine

IRRITANCY OF MATERIAL..........Moderate

SENSITIZATION TO MATERIAL......ND

CARCINOGENICITY................None known.

REPRODUCTIVE TOXICITY..........None known.

TERATOGENICITY......None known.MUTAGENICITY....None known.

SYNERGISTIC PRODUCTS...........None Known

SECTION Vll PREVENTIVE MEASURES

HAND PROTECTION.........Rubber or vinyl gloves when handling

EYE PROTECTION....Chemical goggles or face shield.

RESPIRATORY PROTECTION.........NIOSH approved respirator with Chlorine cartridges

FOOT WEAR.......Impermeable   CLOTHING........Rubber apron

ENGINEERING CONTROLS...........Local exhaust ventilation

LEAK AND SPILL PROCEDURE.......Ventilate area. Dyke area and contain spill. Absorb using inert material. (Sand). For recovery pump into polyethylene container. Very small spills flush into sewer with large volumes of water.

WASTE DISPOSAL.................Dispose in accordance with local, provincial and federal regulations

HANDLING PROCEDURES AND EQUIPMENT..Avoid contact with eyes,skin or clothes.Wash thoroughly after handling.

STORAGE REQUIREMENTS...........Store in a cool dry area. Keep away from acids and incompatibles. Do not freeze.

SECTION Vlll FIRST AID MEASURES

Eye Contact: Wash eyes with water for a minimum of 30 minutes or until no evidence of the chemical remains. Hold eyelids open during flushing. Seek immediate medical attention.

Skin Contact: Remove contaminated clothing. Wash skin with water for at least 30 minutes, using soap if available. Obtain medical attention immediately.

Inhalation: Remove person to fresh air. If not breathing, give artificial respiration. If breathing is difficult, get immediate medical attention.

Ingestion: Rinse mouth with water. Do not induce vomiting. Do not give anything by mouth to an unconscious person. If vomiting occurs spontaneously, keep head below hips to prevent aspiration of liquid into the lungs. Seek immediate medical attention.

Notes To Physician: Due to the severely irritating or corrosive nature of the material, swallowing may lead to ulceration and inflammation of the upper alimentary tract with hemorrhage and fluid loss. Also, perforation of the esophagus or stomach may occur, leading to mediastinitis or peritonitis and the resultant complications.

ADDITIONAL INFORMATION

WHMIS CLASSIFICATION....CLASS E , Class D div 2 B

TDG CLASSIFICATION........NR

SHIPPING NAME:..NA

PIN..............NA	PACKING GROUP...NA

HAZARD RATING: HEALTH:2   FIRE:0   REACTIVITY:1   SPECIAL:0

HAZARD RATING SCALE: 0=MINIMAL, 1=SLIGHT, 2=MODERATE, 3=SERIOUS, 4=SEVERE.  NA=NOT APPLICABLE, ND=NO DATA AVAILABLE, NE=NOT ESTABLISHED, NR NOT REGULATED.

PREPARED BY: LAB GROUP   DATE: May 8, 2009

TEL: 905-678-9559

DISCLAIMER: THE INFORMATION CONTAINED HEREIN IS COMPILED FROM SOURCES BELIEVED TO BE RELIABLE. THE MANNER AND CONDITIONS OF USE AND HANDLING MAY, INVOLVE OTHER AND ADDITIONAL CONSIDERATIONS. WE ACCEPT NO RESPONSIBILITY FOR THE ACCURACY, SUFFICIENCY, RELIABILITY OR FOR ANY LOSS OR INJURY RESULTING FROM THE USE OF THE INFORMATION.